## Slide 1: 12 bit Asynchronous Counter
Manjur Muntasir
1906150
Khondaker Nafis Ahmed
1906147
Fahim Shahriar Anim
1906178
Project Group 2
Section C1
July 2023
Project Presentation
EEE -468 : VLSI Laboratory
Section: G2
Shahriyer Hasan
1906128
Abid Abdullah
1906108

## Slide 2: Outline
Introduction
Implementation
Output Analysis
Result Discussion
Conclusion

## Slide 3: Introduction
A 12-bit asynchronous counter, also known as a ripple counter, is a type of digital counter used in electronics to count pulses or events
This allows the counter to count from 0 to 212 −1, or 0 to 4095 in decimal.
All control signals (Load, Up_down, Reset, Enable) are asynchronous here.

## Slide 4: Implementation Plan
Design Code
Verification using Directed and Layered Testbench
RTL Synthesis
PnR Analysis
Optimization

## Slide 5: Implementation Plan
Cadence CAD Tools
NCSim for simulation
Sim vision for visualization
Genus for RTL synthesis
Innovus for PnR

## Slide 6: Implementation
Design Problem

## Slide 7: Implementation
Final Design Verilog
module counter(clk, reset, up_down, load, data, count, enable);
//define input and output ports
input clk, reset, load, up_down, enable;
input [11:0] data;
output reg [11:0] count;
//always block will be executed at each and every positive edge of the clock
always@(posedge reset)
begin
if(!enable) count<=count;
else count<=0;
end
always@(negedge reset)
begin
if(!enable) count<=count;
else if(load) count<=data;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(posedge load)
begin
if(!enable) count<=count;
else if(!reset) count<=data;
end
always@(negedge load)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(posedge clk)
begin
if(!enable) count<=count;
else if(!reset & !load)
begin
if(up_down==1) count<=count+1;
else if(up_down==0) count<=count-1;
end
end
always@(posedge up_down)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(load) count<=data;
else count<=count+1;
end
always@(negedge up_down)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(load) count<=data;
else count<=count-1;
end

## Slide 8: Implementation
Final Design Verilog
always@(posedge enable)
begin
if(reset) count<=0;
else if(load) count<=data;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(data)
if(load & !reset) count<=data;
endmodule

## Slide 9: Implementation
Design Difficulties
1. Multiple inputs transition at the same time
module counter(clk, reset, up_down, load, data, count, enable);
//define input and output ports
input clk, reset, load, up_down, enable;
input [3:0] data;
output reg [3:0] count;
always@(posedge reset)
if(enable)
begin
count<=0;
end
always@(posedge load)
if(enable)
begin
count<=data;
end
always@(posedge up_down or negedge up_down)
if(enable)
begin
if(up_down) count<=count+1;
else count<=count-1;
end
//always block will be executed at each and every positive edge of the clock
always@(posedge clk)
if(enable)
begin
//if(reset) count <= 0; //Set Counter to Zero
//else if(load) count <= data; //load the counter with data value
if(up_down) count <= count + 1; //count up
else count <= count - 1; //count down
end
endmodule

## Slide 10: Implementation
Design Difficulties
2. Reset, Load or Up-Down ON for a long time
module counter(clk, reset, up_down, load, data, count, enable);
//define input and output ports
input clk, reset, load, up_down, enable;
input [11:0] data;
output reg [11:0] count;
logic r=0;
logic l=0;
logic ud=up_down;
//always block will be executed at each and every positive edge of the clock
always@(posedge clk or posedge reset or posedge load or posedge up_down or negedge up_down)
begin
if(enable)
begin
if(reset==1 & r==0)
begin
count<=0;
r=1;
end
else if(load==1 & l==0)
begin
count<=data;
l=1;
end
else if(up_down==1 & ud==0)
begin
count<=count+1;
ud=1;
end
else if(up_down==0 & ud==1)
begin
count<=count-1;
ud=0;
end
else if(up_down==1)
begin
count<=count+1;
ud=1;
end
else if(up_down==0)
begin
count<=count-1;
ud=0;
end
if(reset==0) r=0;
else r=1;
if(load==0) l=0;
else l=1;
end
else count<=count;
end
endmodule

## Slide 11: Implementation
Design Difficulties
3. More than one posedge or negedge inputs not allowed in always
module counter(clk, reset, up_down, load, data, count, enable);
//define input and output ports
input clk, reset, load, up_down, enable;
input [11:0] data;
output reg [11:0] count;
//always block will be executed at each and every positive edge of the clock
always@(posedge reset)
begin
if(!enable) count<=count;
else count<=0;
end
always@(negedge reset)
begin
if(!enable) count<=count;
else if(load) count<=data;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(posedge load)
begin
if(!enable) count<=count;
else if(!reset) count<=data;
end
always@(negedge load)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(posedge clk)
begin
if(!enable) count<=count;
else if(!reset & !load)
begin
if(up_down==1) count<=count+1;
else if(up_down==0) count<=count-1;
end
end
always@(posedge up_down)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(load) count<=data;
else count<=count+1;
end
always@(negedge up_down)
begin
if(!enable) count<=count;
else if(reset) count<=0;
else if(load) count<=data;
else count<=count-1;
end
always@(posedge enable)
begin
if(reset) count<=0;
else if(load) count<=data;
else if(up_down) count<=count+1;
else if(!up_down) count<=count-1;
end
always@(data)
if(load & !reset) count<=data;
endmodule

## Slide 12: Implementation
Directed Testbench
module counter_tb;
reg clk,reset,load,up_down, enable;
reg [11:0] data;
wire [11:0] count;
// instance counter design
counter ct_1(.clk(clk), .reset(reset), .load(load), .up_down(up_down), .enable(enable), .data(data), .count(count));
//clock generator
initial
begin
clk = 1'b0;
repeat(30) #3
clk= ~clk;
end
//insert all the input signal
initial
begin
reset=1'b1; #7
reset=1'b0; #33
reset=1'b1; #2
reset=1'b0;
end
initial
begin
enable=1'b1; #12
enable=1'b0; #22
enable=1'b1;
end
initial
begin
load=1'b1; #18
load=1'b0; #22
load=1'b1; #8
load=1'b0; #12
load=1'b1; #10
load=1'b0;
end
initial
begin
up_down=1'b1; #40
up_down=1'b0; #20
up_down=1'b1; #8
up_down=1'b0; #10
up_down=1'b1; #8
up_down=1'b0;
end
initial
begin
data=12'b100011001000; #14
data=12'b110100111100; #2
data=12'b111100001111; #20
data=12'b101001011010; #8
data=12'b110000111100;
end
//monitor all the input and output ports at times when any inputs changes its state
initial
begin
$monitor("time=%0d, reset=%b, load=%b, up_down=%b, data=%d, count=%d", $time, reset, load, up_down, data, count);
end
initial
begin
$dumpfile("dump.vcd");
$dumpvars();
#100
$finish;
end
endmodule

## Slide 13: Implementation
Directed Testbench

## Slide 14: Implementation
Layered Testbench – Testbench.sv
`include "testcase01.sv"
//`include "test.sv"
`include "interface.sv"
module testbench;
bit clk;
initial begin
forever #5 clk =~clk;
end
int tnum=30;
counter_if countif(clk);
test test01(tnum,countif);
initial begin
$dumpfile("dump.vcd");
$dumpvars;
#200;
$finish;
end
counter DUT (
.reset(countif.reset),
.up_down(countif.up_down),
.load(countif.load),
.enable(countif.enable),
.data(countif.data),
.count(countif.count),
.clk(clk)
);
endmodule
Layered Testbench – Interface.sv
interface counter_if(input clk);
logic reset,load, up_down, enable;
logic [11:0] data;
logic [11:0] count;
clocking driver_cb @(negedge clk);
default input #0 output #0;
output reset,load, up_down, enable, data;
endclocking
clocking mon_cb @(clk, reset, enable, load, up_down, data);
default input #0 output #0;
input reset,load, up_down, enable, data;
input count;
endclocking
modport DRIVER (clocking driver_cb, input clk);
modport MONITOR (clocking mon_cb, input clk);
endinterface

## Slide 15: Implementation
Layered Testbench – Scoreboard.sv
class scoreboard;
mailbox driv2sb;
mailbox mon2sb;
transaction d_trans;
transaction m_trans;
event driven;
function new(mailbox driv2sb, mon2sb);
this.driv2sb=driv2sb;
this.mon2sb=mon2sb;
endfunction
task main(input int tnum);
$display("------------------Scoreboard Test Starts--------------------");
repeat(tnum) begin
m_trans=new();
mon2sb.get(m_trans);
report();
if(m_trans.count != d_trans.count)
$display("time:%d, Failed : reset=%d up_down=%d load=%d enable=%d data=%d Expected out=%d Resulted out=%d",$time, d_trans.reset,d_trans.up_down, d_trans.load, d_trans.enable, d_trans.data, d_trans.count,
m_trans.count);
else
$display("time:%d, Passed : reset=%d up_down=%d load=%d enable=%d data=%d Expected out=%d Resulted out=%d",$time, d_trans.reset,d_trans.up_down, d_trans.load, d_trans.enable, d_trans.data, d_trans.count, m_trans.count);
end
$display("------------------Scoreboard Test Ends--------------------");
endtask:main
task report();
d_trans=new();
driv2sb.get(d_trans);
if (d_trans.enable==1)
begin
if(d_trans.reset==1) d_trans.count=0;
else if(d_trans.load==1) d_trans.count=d_trans.data;
else if(d_trans.up_down==1) d_trans.count=d_trans.count+1;
else if(d_trans.up_down==0) d_trans.count=d_trans.count-1;
end
else d_trans.count=d_trans.count;
endtask:report
endclass:scoreboard

## Slide 16: Implementation
Layered Testbench – Transaction.sv
class transaction;
bit [11:0] data = 5;
rand bit reset;
rand bit up_down;
bit enable = 1;
rand bit load;
bit [11:0] count;
endclass:transaction
Layered Testbench – Waveform

## Slide 17: Implementation
Layered Testbench

## Slide 18: Implementation
Layered Testbench

## Slide 19
SYNTHESIS

## Slide 20: Synthesis
Synthesis:
Synthesis after using syn_map:

## Slide 21: Synthesis
TCL code:
#run Genus in Legacy UI if Genus is invoked with Common UI
::legacy::set_attribute common_ui false / ;
if {[file exists /proc/cpuinfo]} {
sh grep "model name" /proc/cpuinfo
sh grep "cpu MHz" /proc/cpuinfo
}
puts "Hostname : [info hostname]"
##############################################################################
### Preset global variables and attributes
##############################################################################
set DESIGN counter2
set SYN_EFF medium
set MAP_EFF medium
set OPT_EFF medium
# Directory of PDK
#set pdk_dir /home/wsadiq/buet_flow/GPDK045
set pdk_dir /home/cad/VLSI2Lab/Digital/library/
#set_attribute init_lib_search_path $pdk_dir/gsclib045/timing
#set_attribute init_hdl_search_path /home/wsadiq/buet_flow/rtl
set_attribute init_lib_search_path $pdk_dir
#set_attribute init_hdl_search_path ../../rtl
##Set synthesizing effort for each synthesis stage
set_attribute syn_generic_effort $SYN_EFF
set_attribute syn_map_effort $MAP_EFF
set_attribute syn_opt_effort $OPT_EFF
#set_attribute library "\
slow_vdd1v0_basicCells_hvt.lib \
slow_vdd1v0_basicCells.lib \
slow_vdd1v0_basicCells_lvt.lib"
set_attribute library "\
slow_vdd1v0_basicCells.lib"
set_dont_use [get_lib_cells CLK*]
set_dont_use [get_lib_cells SDFF*]
set_dont_use [get_lib_cells DLY*]
set_dont_use [get_lib_cells HOLD*]
# If you dont want to use LVT uncomment this line
#set_dont_use [get_lib_cells *LVT*]
####################################################################
### Load Design
#####################################################################
###source verilog_files.tcl
read_hdl "\
${DESIGN}.v"
elaborate $DESIGN
puts "Runtime & Memory after 'read_hdl'"
time_info Elaboration
check_design -unresolved
####################################################################
### Constraints Setup
#####################################################################
read_sdc counter2.sdc
report timing -encounter >> reports/${DESIGN}_pretim.rpt
####################################################################################################
### Synthesizing to generic
####################################################################################################
syn_generic
puts "Runtime & Memory after 'syn_generic'"
time_info GENERIC
report datapath > reports/${DESIGN}_datapath_generic.rpt
generate_reports -outdir reports -tag generic
write_db -to_file ${DESIGN}_generic.db
report timing -encounter >> reports/${DESIGN}_generic.rpt
##This synthesizes your code
syn_map
## This writes all your files
write -mapped > counter2_synth.v
## THESE FILES ARE NOT REQUIRED, THE SDC FILE IS A TIMING FILE
write_script > script

## Slide 22
Reports

## Slide 23
Variable: CLOCK PERIOD

## Slide 25
Period increases and power decreases but speed also decreases

## Slide 26
Variation of power in LOW and HIGH effort is 0.02 mW, but cell area is very high in Low effort

## Slide 27
Variable: SETUP TIME/ HOLD TIME/ INPUT DELAY/ OUTPUT DELAY

## Slide 28
Variable: SETUP TIME/ HOLD TIME/ INPUT DELAY/ OUTPUT DELAY
Clock Period: 10ns

## Slide 29
Power and Area do not change with respect to a change in the mentioned parameters. However, different effort gives different values of Power and area

## Slide 33
Variable: SETUP TIME/ HOLD TIME/ INPUT DELAY/ OUTPUT DELAY
Clock Period: 50ns

## Slide 36
Remarks:
1. Low effort has lower power consumption
2. However low effort requires highest cell area
3. We can select medium or high effort since power consumption is not much higher (0.004 to 0.002 mW range), which allows us to reduce cell area
4. Power consumption shows exponentially decaying behavior with time period. We can choose clock period = 10ns (Power consumption curve almost saturates from this point).

## Slide 37
Optimized Design
Parameters | Designed Value
Clock Period | 10ns
Setup Time | 3ns
Hold Time | 2ns
Input Delay | 0.4ns
Output Delay | 0.6ns

## Slide 38
PHYSICAL DESIGN

## Slide 39
Default Layout: Area – 41.2 x 39.33, Spacing – 0.84, Set-to-set distance - 2

## Slide 40
Default Layout: Area – 41.37 x 39.33, Spacing – 0.84, Set-to-set distance - 2

## Slide 41
Default Layout: Area – 41.37 x 39.33, Spacing – 0.84, Set-to-set distance - 2

## Slide 42
Default Layout: Area – 41.37 x 39.33, Spacing – 0.84, Set-to-set distance - 2

## Slide 43
Default Layout: Area – 41.37 x 39.33, Spacing – 0.15, Set-to-set distance - 2

## Slide 44
Default Layout: Area – 41.37 x 39.33, Spacing – 0.6, Set-to-set distance - 2

## Slide 45
Final Optimized Layout: Area – 60 x 50, Set-to-set distance – 2, Spacing – 0.84

## Slide 46
Final Optimized Layout: Area – 39 x 37, Set-to-set distance – 2, Spacing – 0.6

## Slide 47
Final Optimized Layout: Area – 39 x 37, Set-to-set distance – 2, Spacing – 0.6

## Slide 48
Final Optimized Layout: Area – 39 x 37, Set-to-set distance – 2, Spacing – 0.6

## Slide 49
Final Optimized Layout: Area – 39 x 37, Set-to-set distance – 1, Spacing – 0.6
Final Optimized Layout: Area – 39 x 37, Set-to-set distance – 3, Spacing – 0.6

## Slide 50
Optimized Design
Parameters | Designed Value
Width | 39
Height | 37
Set-to-set distance | 2
Spacing | 0.6
Density | 94.881%

## Slide 51
THANK YOU